Locker Shelf Instructions

Materials

Four piano hinges – 4cm x 30cm

Two ½” plywood boards 30cm x 80cm – sanded edges

Two ½” plywood boards 30cm x 27cm – sanded edges

Assembly

- Measure and mark with a line across the width of the two 30cm x 80cm  boards, 26cm up from the bottom on the inside of each board

- Measure and mark with a line across the width of the two 30cm x 80cm  boards, 58cm up from the bottom on the inside of each board

- Stand the 30cm x 80cm boards parallel to one another, lengthwise, leaving space in between to set in the smaller boards, which will be used as shelves

- Attach the bottom shelf at the 26cm line using the piano hinges.  The piano hinge on the right should be screwed into the top of the shelf.  The hinge on the left should be installed under the shelf. (see diagram)

- Attach the upper shelf at the 58cm line using the piano hinges.  The piano hinge on the right should be screwed into the top of the shelf.  The hinge on the left should be installed under the shelf. (see diagram)

The shelving unit should be able to fold flat!